## Slide 1: Distributed Generation system

## Slide 2: Outline:
What is Distributed Generation?
Advantages of DG
Block Diagram of DG
Synchronous Generator
  Permanent Magnet Synchronous Machines
  Assumptions and Calculations
  Outputs
3-ф DC-AC Inverter
  Specifications
  Pulse Width Modulation
Low Pass Filter

## Slide 3: What is Distributed Generation ??
An active small scale generation at distribution level.
Generation of electricity by facilities sufficiently smaller than central plants, so as to allow interconnection at nearly any point in the power system , as Distributed Resource.
Yield power in capacities that range from a fraction of a kilowatt [kW] to about 100 megawatts [MW].
Often include renewable energy technologies that are site specific, such as wind turbines, geothermal energy production, solar systems (photovoltaic and combustion), and some hydro-thermal plants.

## Slide 4: Advantages of DG
It reduces the power losses while transmission as they are very near to the load.
Increased electric system reliability
Emergency supply of power
Reduction of peak power requirements
Provision of ancillary services like regulation, reactive power and black start etc.,

## Slide 5
CG
DG

## Slide 6: Synchronous Generator
Synchronous refers to the fact that the rotor and magnetic field rotate with the same speed.
Ideal for power generation: Uniform, controllable waveform output
A permanent magnet synchronous Machine (PMSM) has a fixed excitation provided by a permanent magnet instead of coil.
The prime mover of this generator (In our case) is the combination of LP and HP Turbines at thermal power station.

## Slide 7: Why a PMSM ??
Simplicity in design
No system is required for Excitation.
Minimum Energy Dissipation
As per our goal to reduce environmental damage, this machine helps a lot.

## Slide 8: Assumptions and Calculations
It is assumed that the generator is in steady state condition.
We obtain Quadrature current using the torque.
For the 1st iteration, the Direct and Quadrature currents are assumed to be 0.
Again for the 1st iteration, Quadrature and Direct voltage will be calculated using only the speed voltages..
Now using inverse park, we get phase voltages and currents.

## Slide 9: Flow Diagram

## Slide 12: 3-ф DC-AC Inverter

## Slide 13: MOSFET vs IGBT

## Slide 14: MOSFET vs IGBT
Two of most important modern devices
IGBTs excellent for high power, low frequency devices: Some of the advantages of FET and BJT combined into one device
MOSFETs find most frequent “general use”: Excellent for high frequency operation, and consume very little power. Any low or medium power system should use FET

## Slide 15: Specifications
Ideal MOSFETS with anti parallel DIODES are employed to switch DC Source
  3 legs with two complimentary switches per leg
  Operated in Saturated / Off regions
  No Delays
  No Leakage or Inrush current
Operational Amplifiers are used to generate PWM for switches
  Sinusoidal Input with a fundamental frequency of 60Hz
  Saw tooth waveform for control of PWM
  Three stages with 120˚ phase shift

## Slide 16: Pulse Width Modulation (PWM):

## Slide 18: HIGH FREQUENCY COMPONENTS !!
HIGH FREQUENCY COMPONENTS !!

## Slide 19: Low Pass Filter
To eliminate HIGH FREQUENCY COMPONENTS from the output of converter.
Out of all the available topologies, LCL has been chosen to eliminate 3rd order harmonics and to deliver more stable outputs.

## Slide 20: Inverter with LPF

## Slide 24: Supporting GRID
Before connecting our secondary generator to the grid, following parameters have to match :
              Phase Sequence
              Voltage Magnitude
              Frequency
              Phase Angle

## Slide 26: DG Model

## Slide 30: Conclusion
Reduced Load by 50% on Thermal Power Stations to lessen environmental Damage.
Another 50% of the load is supplied using DC-AC inverter locally.
High frequency components from the inverter are eliminated using LPF.
All the required steps are taken before connecting the local generator to the grid.

## Slide 31: THANK YOU !!